## Slide 1: Bluetooth Low Energy (BLE) for iOS
Nicolas Flacco
March 5, 2014

## Slide 2: About Me
Engineer on Client Analytics Team
Worked on NFC and networking on iOS in previous jobs
Have been working with BLE and iBeacon since Q4 2013.
Current personal project: Peer to peer mesh network using BLE
Notes: I’m fairly new to this, but I’ve worked on some very complicated Bluetooth stuff so I can save you lots of trouble.

## Slide 3: Requirements
Familiarity with Objective-C
XCode 5.0+
Developer account (run app on iOS device)
An iOS device (simulator cannot do BLE)
Notes: -This is not an intro to building IOS apps
-You cannot do this on the simulator. The simulator cannot do BLE.

## Slide 4: Course Outline
Introduction
What is BLE?
Apple’s CoreBluetooth Framework
Build a working BLE app
Conclusion
Notes: We will not discuss iBeacons- they are sufficient material for another day

## Slide 5: What is BLE?
BLE is a new part of the Bluetooth Spec
It centers around low energy service discovery and data transmission
Devices broadcast their services, and other devices find them without needing to pair or do any configuration

## Slide 6: BLE
Subscribe to HR Data!
Advertise HR Data
Notes: The classic application is a hear rate monitor which an app on your phone discovers, connects to, and subscribes to data from

## Slide 7: Bluetooth vs BLE
Bluetooth Classic
Scatternet
High throughput
High power consumption
High latency to connect to another device and send data
Devices must be paired
BLE
Client-server
Low throughput
Low power consumption
Low latency
No pairing
Notes: No pairing opens up really cool use cases. You can walk down the street and your smartphone is in your pocket and it can interact with BLE devices- discover them, get data from them, etc.
----- Meeting Notes (3/12/14 16:18) -----
Security model.
High throughput/power consumption - relative to BLE

## Slide 8: CoreBluetooth Framework
Central (Client)
  Discovers peripherals and connects to them
Peripheral (Server)
  Advertises itself
  Services, which have Characteristics
  Central can subscribe to characteristics or read/write to them
Notes: This class focuses on CoreBluetooth. I will cover iBeacons in another class
A beacon is a peripheral.
----- Meeting Notes (3/12/14 16:18) -----
Does CoreBluetooth use BLE?

## Slide 9: CoreBluetooth Use Case
Central
Peripheral
Notes: The HR monitor could have a HR monitor service, with a BPM notification characteristic, which sends out data, let’s say, every second
----- Meeting Notes (3/12/14 16:18) -----
You could stream data, but you have to write your own interface on a message oriented interface -> do on previous page

## Slide 10: Services and Characteristics
A BLE device can have multiple services, each with multiple characteristics
Services AND Characteristics are identified by unique IDs
Characteristics come in two flavors:
  Notification
  Read and/or write
Notes: ----- Meeting Notes (3/12/14 16:18) -----
Steal diagram of characteristic and service diagram from other guy's presentation

## Slide 11: Central-Peripheral Lifecycle
Peripheral advertises a service with certain characteristics
Central discovers advertisement
Central connects to peripheral
Central discovers services
Central discovers characteristics
Central subscribes or reads from/writes to a characteristic
Central disconnects
Notes: This class focuses on CoreBluetooth. I will cover iBeacons in another class
----- Meeting Notes (3/12/14 16:18) -----
Cast this in terms of a diagram

## Slide 12: Demo-Zeit!
I will now demonstrate the working code that you will build in this class.

## Slide 13: Coding-Zeit!
Clone this repo:
    git clone https://github.com/a34729t/SimpleCentral
Check out the branch for this class:
    git checkout twitteru
Open up the project file in Xcode
Simple UI: ViewController and Storyboard
The files you are going to work with are
  CentralManager.h/.m
  BLEInfo.h
Notes: You will have to complete a bunch of functions in CentralManager.m

## Slide 14: BLEInfo.h
Configuration File
Define CBUUIDs so we can discover the service and the characteristics advertised by our peripheral
  SERVICE_CBUUID
  NOTIFY_CHARACTERISTIC_CBUUID
Notes: I define the CBUUIDs directly, as opposed to just the strings because it’s very easy in the CentralManager to use the strings by accident instead of wrapping them in CBUUIDs

## Slide 15: CentralManager.h
Protocol for discovering peripherals, and receiving data from them (implemented by UI)
Public methods
  Get singleton instance of CentralManager
  Start scanning for peripherals
  Stop scanning
Notes: Note that scanning and detecting are used interchangeably in the literature

## Slide 16: CentralManager.m
I have implemented the constructors and a few other utility methods
I will guide you through the implementation of everything else
  Delegates for CBCentralCentralManager
  Delegates for CBPeripheral (connected Peripheral)
I will add log messages to everything- I highly encourage you to do the same
Notes: NOTE: CBPeripheral is different than CBPeripheralManager (one is used for connecting to Peripherals, and one is for being a peripheral)

## Slide 17: - (id)init
We create a queue for the CBCentralManager
This means delegates also fire on this queue- any calls to the UI need to be on the main queue
We also create a Dictionary to hold Peripherals we connect to. Why?
  Peripherals need to be retained as soon as they discovered
  We map the Peripheral to a NSMutableArray, which functions as queue for incoming data from that Peripheral (this allows us to handle multiple peripherals)

## Slide 18: Peripheral Management
- (void)addPeripheral:(CBPeripheral *)peripheral
- (void)removePeripheral:(CBPeripheral *)peripheral
- (NSMutableArray *)getPeripheralQueue:(CBPeripheral *)peripheral

## Slide 19: Start and Stop Scanning
We have to scan for the Peripheral with a given Service CBUUID
We also give it an option to ignore duplicates
Notes: What does it mean to ignore duplicates? There is a constant barrage of advertisements, so you don’t want these, unless you want constant proximity updates.

## Slide 20: centralManagerDidUpdateState
I’ve enumerated all the states for you
We need to add a call to start scanning once BLE is powered on
A common mistake is to start doing stuff before we are in powered on state- this causes problems because the hardware is not ready

## Slide 21: didDiscoverPeripheral
You receive
  Information about the peripheral itself
  A dictionary of data the peripheral is advertising
  RSSI (Signal strength), higher number (ie less negative) means stronger signal
Don’t try to connect to a weak signal
Add the Peripheral to your dictionary so it is retained. Otherwise you will get a dealloc error message
Attempt a connection
Fire delegate on main thread to notify UI of discovery
Notes: RSSI = Received Signal Strength Indication
You have to retain peripheral BEFORE you connect

## Slide 22: Connection Outcomes
didFailToConnectPeripheral
  Remove Peripheral
didDisconnectPeripheral
  Remove Peripheral
didConnectPeripheral
  Set the CentralManager.m as the delegate of the Peripheral
  Discover Services, using Service_CBUUID

## Slide 23: didDiscoverServices
Discovered Peripheral that has a given Service, but we need to loop through all its Services to access this Service
The only Service we can talk to (even if we had it previously) is the Service returned by the delegate
But first, check error case
Once correct Service has been identified, discoverCharacteristics
Notes: We get all

## Slide 24: didDiscoverCharacteristicsForService
Similar to DiscoverServices, we need to loop through all Characteristics of Service
And we need to check the error case
Once we have identified the Characteristic we want, tell the Peripheral to notify us when the value of the Characteristic is updated

## Slide 25: didUpdateNotificationStateForCharacteristic
If the characteristic is notifying, great
If it isn’t, then we should disconnect

## Slide 26: didUpdateValueForCharacteristic
Check for errors
Make sure the characteristic is the one we are subscribed to
Convert the NSData to NSString
Fire a delegate to the UI (on the main thread)

## Slide 27: Messages that are > MTU
Peripheral: Chunk a message into pieces of MTU size + EOM packet
Central: Receive chunked message from a given peripheral, and reassemble it
Fortunately, I’ve already given you a message Queue for each connected Peripheral
Look at the branch chunkmsg for more details

## Slide 28: CBPeripheral is being decalloc’ed while connecting
2014-03-08 09:44:27.096 BLE Echo Client[10022:60b] CoreBluetooth[WARNING] <CBCentralManager: 0x16e4fc10> is not powered on
2014-03-08 09:44:27.100 BLE Echo Client[10022:60b] CM Scanning started
2014-03-08 09:44:27.109 BLE Echo Client[10022:3707] CoreBluetooth BLE hardware is powered on and ready
2014-03-08 09:44:27.143 BLE Echo Client[10022:3707] CM Discovered name:(null) id:50A16740-FD50-4E8D-2195-4C0CB06F2C6D rssi:-37
2014-03-08 09:44:27.146 BLE Echo Client[10022:60b] VC didDiscoverPeripheral:<__NSConcreteUUID 0x16d313c0> 50A16740-FD50-4E8D-2195-4C0CB06F2C6D rssi:-37
2014-03-08 09:44:27.148 BLE Echo Client[10022:3707] CoreBluetooth[WARNING] <CBPeripheral: 0x16e2c8c0 identifier = 50A16740-FD50-4E8D-2195-4C0CB06F2C6D, Name = "(null)", state = connecting> is being dealloc'ed while connecting

## Slide 29: We’re done
Email me (nflacco@twitter.com) or drop by my desk if you have feedback, questions, ideas, etc.
I will try to get some screencasts for the remote folks

## Slide 30: Future Courses
I hope to teach classes on the following subjects:
  Peripherals, and background Peripheral discovery
  iBeacons (building on our work with Centrals and Peripherals, but using the CoreLocation framework)
  Advanced applications of these technologies (p2p mesh networks, indoor mapping)