## Slide 1: Bluetooth Low Energy (BLE) for iOS
Nicolas Flacco
March 5, 2014

## Slide 2: About Me
Engineer on Client Analytics Team
Worked on NFC and networking on iOS in previous jobs
Have been working with BLE and iBeacon since Q4 2013.
Current personal project: Peer to peer mesh network using BLE
Notes: I’m fairly new to this, but I’ve worked on some very complicated Bluetooth stuff so I can save you lots of trouble.

## Slide 3: Requirements
Familiarity with Objective-C
XCode 5.0+
Developer account (run app on iOS device)
An iOS device (simulator cannot do BLE)
Notes: -This is not an intro to building IOS apps
-You cannot do this on the simulator. The simulator cannot do BLE.

## Slide 4: Course Outline
Introduction
What is BLE?
Apple’s CoreBluetooth Framework
Build a working BLE app
Conclusion

## Slide 5: What is BLE?
BLE is a new part of the Bluetooth Spec
It centers around low energy service discovery and data transmission
Devices broadcast their services, and other devices find them without needing to pair or do any configuration

## Slide 6: BLE
Subscribe to HR Data!
Advertise HR Data
Notes: The classic application is a hear rate monitor which an app on your phone discovers, connects to, and subscribes to data from

## Slide 7: Bluetooth vs BLE
Bluetooth Classic
Scatternet
High throughput
High power consumption
High latency to connect to another device and send data
Devices must be paired
BLE
Client-server
Low throughput
Low power consumption
Low latency
No pairing
Notes: No pairing opens up really cool use cases. You can walk down the street and your smartphone is in your pocket and it can interact with BLE devices- discover them, get data from them, etc.

## Slide 8: CoreBluetooth Framework
Central (Client)
  Discovers peripherals and connects to them
Peripheral (Server)
  Advertises itself
  Services, which have Characteristics
  Central can subscribe to characteristics or read/write to them
Notes: This class focuses on CoreBluetooth. I will cover iBeacons in another class
A beacon is a peripheral.

## Slide 9: CoreBluetooth Use Case
Central
Peripheral
Notes: The HR monitor could have a HR monitor service, with a BPM notification characteristic, which sends out data, let’s say, every second

## Slide 10: Services and Characteristics
A BLE device can have multiple services, each with multiple characteristics
Services AND Characteristics are identified by unique IDs
Characteristics come in two flavors:
  Notification
  Read and/or write

## Slide 11: Central-Peripheral Lifecycle
Peripheral advertises a service with certain characteristics
Central discovers advertisement
Central connects to peripheral
Central discover services
Central discovers characteristics
Central subscribes or reads from/writes to a characteristic
Central disconnects
Notes: This class focuses on CoreBluetooth. I will cover iBeacons in another class

## Slide 12: Demo-Zeit!
I will now demonstrate the working code that you will build in this class.

## Slide 13: Coding-Zeit!
Clone this repo:
    git clone https://github.com/a34729t/SimpleCentral
Check out the branch for this class:
    git checkout twitteru
Open up the project file in Xcode
Simple UI: ViewController and Storyboard
The files you are going to work with are
  CentralManager.h/.m
  BLEInfo.h
Notes: You will have to complete a bunch of functions in CentralManager.m

## Slide 14: BLEInfo.h
Configuration File
Define CBUUIDs so we can discover the service and the characteristics advertised by our peripheral
  SERVICE_CBUUID
  NOTIFY_CHARACTERISTIC_CBUUID
Notes: I define the CBUUIDs directly, as opposed to just the strings because it’s very easy in the CentralManager to use the strings by accident instead of wrapping them in CBUUIDs

## Slide 15: CentralManager.h
Protocol for discovering peripherals, and receiving data from them (implemented by UI)
Public methods
  Get singleton instance of CentralManager
  Start scanning for peripherals
  Stop scanning
Notes: Note that scanning and detecting are used interchangeably in the literature

## Slide 16: CentralManager.m
I have implemented the constructors and a few other utility methods
I will guide you through the implementation of everything else
I will add log messages to everything- I highly encourage you to do the same

## Slide 17: - (id)init
We create a thread for the CentralManager
This means we need to fire delegates back into the main thread
We also create a Dictionary to hold Peripherals we connect to. Why?
  Peripherals need to be retained
  We map the Peripheral to a NSMutableArray, which functions as queue for incoming data from that Peripheral

## Slide 18: Peripheral Management
- (void)addPeripheral:(CBPeripheral *)peripheral
- (void)removePeripheral:(CBPeripheral *)peripheral
- (NSMutableArray *)getPeripheralQueue:(CBPeripheral *)peripheral

## Slide 19: Start and Stop Scanning
We have to scan for the Peripheral with a given Service CBUUID
We also give it an option to ignore duplicates
Stopping scan is easy

## Slide 20: centralManagerDidUpdateState
I’ve enumerated all the states for you
We need to add a call to start scanning once BLE is powered on
A common mistake is to start doing stuff before we are in powered on state- this causes problems because the hardware is not ready

## Slide 21: didDiscoverPeripheral
You receive
  Information about the peripheral itself
  A dictionary of data the peripheral is advertising
  RSSI (Signal strength), higher number (ie less negative) means stronger signal
Don’t try to connect to a weak signal
Add the Peripheral to your dictionary so it is retained. Otherwise you will get a dealloc error message
Attempt a connection
Fire delegate on main thread to notify UI of discovery
Notes: RSSI = Received Signal Strength Indication
You have to retain peripheral BEFORE you connect

## Slide 22: Connection Outcomes
didFailToConnectPeripheral
  Remove Peripheral
didDisconnectPeripheral
  Remove Peripheral
didConnectPeripheral
  Set the CentralManager as the delegate of the Peripheral
  Discover Services, using Service_CBUUID

## Slide 23: didDiscoverServices
Discovered Peripheral that has a given Service, but we need to loop through all its Services to access this Service
But first, check error case
Once correct Service has been identified, discoverCharacteristics
Notes: We get all

## Slide 24: didDiscoverCharacteristicsForService
Similar to DiscoverServices, we need to walk through all Characteristics of Service
And we need to check the error case
Once we have identified the Characteristic we want, tell the Peripheral to notify us when the value of the Characteristic is updated

## Slide 25: didUpdateNotificationStateForCharacteristic
If the characteristic is notifying, great
If it isn’t, then we should disconnect

## Slide 26: didUpdateValueForCharacteristic
Check for errors
Make sure the characteristic is the one we are subscribed to
Convert the NSData to NSString
Fire a delegate to the UI (on the main thread)

## Slide 27: Messages that are > MTU
Peripheral: Chunk a message into pieces of MTU size + EOM packet
Central: Receive chunked message from a given peripheral, and reassemble it
Fortunately, I’ve already given you a message Queue for each connected Peripheral

## Slide 28: CBPeripheral is being decalloc’ed while connecting
2014-03-08 09:44:27.096 BLE Echo Client[10022:60b] CoreBluetooth[WARNING] <CBCentralManager: 0x16e4fc10> is not powered on
2014-03-08 09:44:27.100 BLE Echo Client[10022:60b] CM Scanning started
2014-03-08 09:44:27.109 BLE Echo Client[10022:3707] CoreBluetooth BLE hardware is powered on and ready
2014-03-08 09:44:27.143 BLE Echo Client[10022:3707] CM Discovered name:(null) id:50A16740-FD50-4E8D-2195-4C0CB06F2C6D rssi:-37
2014-03-08 09:44:27.146 BLE Echo Client[10022:60b] VC didDiscoverPeripheral:<__NSConcreteUUID 0x16d313c0> 50A16740-FD50-4E8D-2195-4C0CB06F2C6D rssi:-37
2014-03-08 09:44:27.148 BLE Echo Client[10022:3707] CoreBluetooth[WARNING] <CBPeripheral: 0x16e2c8c0 identifier = 50A16740-FD50-4E8D-2195-4C0CB06F2C6D, Name = "(null)", state = connecting> is being dealloc'ed while connecting

## Slide 29: What are Beacons?
Peripherals
Use the advertising packets to notify users of a unique BLE device
Unique beacon can then be tied to data in a smartphone app (beacon Id -> shoes on sale)
Apple has their own standard, iBeacon, which uses the CoreLocation Framework

## Slide 30: CoreBluetooth Background Mode
To discover peripherals, you must specify one or more Service UUIDs. You cannot do a scan for arbitrary peripherals
Notes: This class focuses on CoreBluetooth. I will cover iBeacons in another class